## Slide 1
中国地质大学（北京）辐射与环境实验室 RADIATION AND ENVIRONMENT LABORATORY
Objective
220Rn concentrations survey was carried out for the first time using a RAD7 portable radon monitor in Zhuhai City and Zhongshan City, covered the total area of 1800 km2 in South China in order to study on 222Rn/220Rn concentrations in soil gas and the correlation between 220Rn concentrations and 232Th activity contents and geological background.
Investigation results
The Level and Distribution of 220Rn Concentrations in Soil Gas in Guangdong Province, China
Wang Nanping, Peng Aimin, Xiao Lei, Chu Xingming, Yin Yin and Qin Chunyan
School of Geophysics and Information Technology and Key Laboratory of Geo-detection (China University of Geosciences, Beijing), Ministry of Education, Beijing 100083, China; Email:npwang@cugb.edu.cn
Instrument and Method
Fig. 2 Contour map 220Rn in soil gas
Conclusion and discussion
(1) The large scale soil radon survey results show that: soil gas 222Rn and 220Rn concentrations are relatively high in the regions of granite outcrops in Zhongshan City, Guangdong Province. 220Rn concentrations in soil were significantly different from that in the surface areas covered by weathered granite of Yanshan Period or Quaternary sediments. The 220Rn concentrations varied between 6.65 and 461 kBq/m3 and the average were 294.42±81.36 and 23.30±25.84 kBqm-3 for weathered granite products and sediments, respectively. The high positive correlation between 220Rn concentrations and 232Th activity contents was found. 220Rn concentrations had no statistically significant variations from depths of 20 to 140 cm with an interval of 20 cm.
(2) 220Rn measurement in the field using a RAD7 radon monitor is feasible, but we found that it is less efficient and normally takes 0.5h for each site if 222Rn is determined simultaneously.
(3) The data should provide valuable reference data for estimating annual effective dose due to absorption of 220Rn and its progenies to the Chinese public.
RAD7 RADON MONITOR
Detector: silicon
Internal sample cell: 0.7 L
Sampling time: 3 min.
Sampling depth: 80 cm
Flow rate: 1 L/min.
Mode: sniff
Geological Overview and Measurement Locations
Fig. 1 Simplified geological map of surveyed area
The surveyed area covered 1800 km2, between 113008' -113037'E and 22010' -22046' N. Geological structure was relatively simple in Zhongshan City and Zhuhai City. The surface deposits that formed since the Late Quaternary mainly consist of arene, medium sized arentilla and arentilla or silty sand and silty clay-clay. The intrusive rocks appear as the Middle and Late Jurassic and Cretaceous biotitic-granite and granodiorite.
Fig. 3 Contour map 222Rn in soil gas
Fig. 4 Contour map of 232Th content
Fig. 6 The scatter plot of 222Rn and 220Rn
Soil collection
A HPGe spectrometer
User ID 2356989